## Slide 1: Introduction to Procedures
Course Code: COE 3205
Dept. of Computer Science
Faculty of Science and Technology
Lab No: | 10 | Week No: | 11 | Semester: | Fall 22-23
Lecturer: | Md. Faruk Abdullah Al Sohan; faruk.sohan@aiub.edu |  |  |  | 
Course Title: Computer Organization & Architecture

## Slide 2: Lab Outline
Terminology of Procedures

## Slide 3: Terminology of Procedures
Overview
The idea is to take the original problem and decompose it into a series of sub problems that are easier to solve than the original.
Like high level languages, an assembly language program can also be structured as a collection of procedures.
One of the procedures is the main procedure containing the entry point to the program.

## Slide 4: Terminology of Procedures
To carry out a task the main procedure calls one of the other procedures. It is also possible for these procedures to call each other or for a procedure to call itself.
    Procedure declaration:
    name PROC type
    ; body of the procedure
    RET
    name ENDP

## Slide 5: Procedure Call and Return
Name is the user defined name of the procedure.
Near: It means that the statement that calls the procedure is in the same segment as the procedure it self.
Far: It means that the calling statement is in the a different segment.
Ret : The ret instruction causes control to transfer back to the calling procedure.
Every procedure should have a ret someplace (except main procedure)

## Slide 6: Procedure Call and Return
Ret : The ret instruction causes control to transfer back to the calling procedure.
Every procedure should have a ret someplace (except main procedure)

## Slide 7: Lab Tasks
Lab Tasks :1
Write a program that to that has three procedures named MAIN, Second and Third. Print one greetings from each of the procedures.
      Sample execution:
      Hi, I am from Main Procedure
      Hi, I am from Second Procedure
      Hi, I am from Second Procedure

## Slide 8: Lab Tasks
Lab Tasks :2
Write a program that prompts the user to enter a character, and on subsequent lines prints its ASCII code in binary, and the number of 1 bit in its ASCII code. Hint: Use 2 Procedures MAIN and TASK
      Sample execution:
      TYPE A CHARACTER: A
      THE ASCII CODE OF A IN BINARY IS: 01000001
      THE NUMBER OF l BITS IS: 2

## Slide 9: Lab Tasks
Lab Tasks :3
Write a program that prompts the user to enter a character, and on subsequent lines prints its ASCII code in binary, and the number of 0 bit in its ASCII code. Hint: Use 2 Procedures MAIN and TASK
      Sample execution:
      TYPE A CHARACTER: A
      THE ASCII CODE OF A IN BINARY IS: 01000001
      THE NUMBER OF 0 BITS IS: 6

## Slide 10: Lab Tasks
Lab Tasks :4
Write a program that gives the following output in DOS. Hint: Use 2 Procedures MAIN and TASK
      Welcome User!!
      Please User Enter Letter 1:
      J
      Please User Enter Letter 2:
      F
      Please User Enter Letter 3:
      K
      Output:
      J F K

## Slide 11: Lab Tasks
Lab Tasks :5
Write a program that gives the following output in DOS. Hint: Use 2 Procedures MAIN and TASK
      Welcome To My Calculator!!
      Please User Enter A Hex Digit (A-F):
      A
      In Decimal it is: 10
      Thank You for using my Calculator
      Have a good day

## Slide 12: Lab Tasks
Lab Tasks :6
Write a program to convert small letter into capital letter. Hint: Use 2 Procedures MAIN and TASK

## Slide 13: Lab Tasks
Lab Tasks :7
Write a program that gives the following output in DOS. Hint: Use 2 Procedures MAIN and TASK
      Welcome To My Calculator!!
      Please User Enter Digit 1:
      2
      Please User Enter Digit 2:
      3
      Output:
      5
      Thank You for using my Calculator

## Slide 14: Lab Tasks
Lab Tasks :8
Write a program that gives the following output in DOS. Hint: Use 2 Procedures MAIN and TASK
      Welcome To My Calculator!!
      Please User Enter Digit 1:
      5
      Please User Enter Digit 2:
      2
      Output:
      3
      Thank You for using my Calculator

## Slide 15
Books
Assembly Language Programing and Organization of the IBM PC
Ytha Yu
Charles Marut

## Slide 16
References
stack, push, pop
  https://www.youtube.com/watch?v=2Gdvz_6m5j8&t=236s
Defining and Using Procedures, CALL and RET
    https://www.youtube.com/watch?v=0dLkvasLSlo