## Slide 1: The Stack and Introduction to Procedures
Course Code: COE 3205
Dept. of Computer Science
Faculty of Science and Technology
Lab No: | 9 | Week No: | 10 | Semester: | Fall 22-23
Lecturer: | Md. Faruk Abdullah Al Sohan; faruk.sohan@aiub.edu |  |  |  | 
Course Title: Computer Organization & Architecture

## Slide 2: Lab Outline
Overview of Stack
PUSH AND PUSHF Instructions
POP AND POPF

## Slide 3: Stack
Overview
The stack segment of a program is used for temporary storage of data and addresses.
The PUSH and POP Instructions are used to add and remove words from the stack respectively.
A stack can be used to reverse a list of data because the last word to be added to the stack Is the first to be removed(LIFO),

## Slide 4: Stack
Overview
A stack is one-dimensional data structure.
Items are added and removed from one end of the structure; that is, it is processed in a "last-in, first-out" manner.
The most recent addition to the stack is called the top of the stack.
A familiar example is a Stack of dishes; the last dish to go on the stack is the top one, and it's the only one that can be removed easily.

## Slide 5: Stack
Overview
A program must set aside a block of memory to hold the stack.
We have been doing this by declaring a stack segment. For example, .STACK lOOH
When the program is assembled and loaded in memory , SS will contain the segment number of the stack segment.
For the preceding Stack declaration, SP, the stack pointer, is initialized to lOOh.
This represents empty stack position.

## Slide 6: Stack
Overview
When the stack is empty, SP contains the offset address of the top of the stack.

## Slide 7: PUSH AND PUSHF Conti..
PUSH is used to add new word to the stack.
The syntax is:
PUSH Source (i.e. PUSH AX)
SP is decreased by 2
A copy of source content is moved to the address specified by SS:SP.

## Slide 8: PUSH AND PUSHF
Initially, SP contains the offset address of memory location.
The first PUSH decreases SP by 2 and point to the LAST WORD in the STACK segment.
PUSHF has no operands and pushes the contents of the flag register to the stack.

## Slide 9: POP AND POPF
POP is used to remove an item from the stack.
The syntax is:
    POP destination (i.e. POP AX)
The content of SS:SP (the top of the stack) Is moved to the destination.
SP is Increased by 2.

## Slide 10: POP AND POPF
The Instruction POPF, pops the top of the stack into the FLAGS register.
There is no effect of PUSH, PUSHF. POP, POPF on the flags.
Note that PUSH and POP are word operations, so a byte Instruction(i.e. PUSH DL or PUSH 2) is illegal.
For INT 21h DOS saves instructions in STACK before execution.

## Slide 11: Lab Tasks
Task: 1
Suppose the register ax = 5, bx =6, Swap the numbers of ax and bx so that ax gets 6 and bx gets 5. use the concept of Stack. Push and Pop instructions must use.
Before Swap:
After Swap :

## Slide 12: Lab Tasks
Task: 2
Suppose that AX= 1234h, BX= 5678h, CX = 9ABCh, and SP= 1 00h. Write an assembly program to find out the contents of AX, BX, CX, and SP after executing the following instructions:
          PUSH AX
          PUSH BX
          XCHG AX,CX
          POP CX
          PUSH AX
          POP BX

## Slide 13: Lab Tasks
Task: 3
Reverse three characters 123, output should look like as follows: Hints, use the concept of push and pop.

## Slide 14: Lab Tasks
Task: 4
Take a string from user. Once user hits enters reverse the string given by the user. Must take input from user. Hints: Use the concept of push and pop.

## Slide 15
Books
Assembly Language Programing and Organization of the IBM PC
Ytha Yu
Charles Marut

## Slide 16
References
stack, push, pop
  https://www.youtube.com/watch?v=2Gdvz_6m5j8&t=236s
Defining and Using Procedures, CALL and RET
    https://www.youtube.com/watch?v=0dLkvasLSlo