## Slide 1: Switch Debouncing and Interrupts
Prepared by Nowshin Alam
Lecturer, AIUB Email: nowshin.alam@aiub.edu

## Slide 2: What is Debouncing?
When the state of a mechanical switch is changed from open to closed and vice versa, there is often a short period of time when the input voltage will jump between HIGH and LOW levels a couple of times before it settles at the applied value. These transitions are called bouncing and getting rid of the effect of the transitions is called debouncing. If you want to input a manual switch signal into a digital circuit, you will need to debounce the signal, so a single press doesn't appear like multiple presses.
Alternatively, when a mechanical switch is flipped/pressed, the metal contacts inside may not open or close cleanly. In the microseconds before the switch achieves a good solid connection, the switch's contacts may "bounce" against each other, turning the switch on and off in rapid succession.

## Slide 3: Why does Bouncing happen?
Bouncing is a result of the physical property of mechanical switches.
Switch and relay contacts are usually made of metallic springs so when a switch is pressed, it is essentially two metal parts that come together. This does not happen immediately, the switch bounces between in-contact (close the contact) and not-in-contact (open the contact) until it finally settles down.
Pull-down Resistor

## Slide 4: Why does Bouncing happen?
Figure shows a simple push switch with a pull-up resistor and its right side, the trace shows the output signal, Vout, when the switch is pressed. As can be seen, pressing the switch does not provide a clean edge. If this signal is used as an input to a digital counter, for example, you will get multiple counts rather than the expected single count.
The same can also occur on the release of a switch.
The problem is that the contacts within the switch don't make contact cleanly, but slightly 'bounce'. The bounce is quite slow, so you can recreate the trace, and the problem quite easily.
Pull-up Resistor

## Slide 5: Why does Bouncing happen?
The bouncing phenomenon is associated with the Single Pole Single Throw (SPST), Single Pole Double Throw (SPDT), and similar other types of toggle switches. The bouncing case data may be analyzed to see how long the switch bounce persists, how wide the individual bounce pulses are, and how many bounces are observed.
It is essential that the technique is not fooled by the occasional noise “glitch” or “spike” caused by-
    Crosstalk,
    EMI (electromagnetic interference)
    RFI (radio frequency interference)
    ESD (electrostatic discharge).

## Slide 6: How does Bouncing happen?
In this diagram, resistor R1 is acting as a pull-up resistor.
  When the switch is open, R1 pulls the NO (Normally Open) contact to a positive (logic 1) value, usually +5 V.
  When the switch is closed, it shorts the NO contact to 0 V (logic 0).

## Slide 7: How does Bouncing happen?
When people push a mechanical switch button, they expect one reaction per push. As the buttons tend to bounce around when pressed and released, this will mess up the signal from them.
For example, we have a button that is connected between a voltage supply and the output probe. We intend to get an output voltage of 5 V (logic 1) when the switch is pressed, and 0 V (logic 0) when it is not pressed. If we probed the output signal coming from the button during the transition from pushing it down to letting go, we expect an immediate and clean transition 0 → 1 → 0. What we end up seeing instead is the picture above. Before the signal settles to a fixed 5 V, it bounces between the two logic states several times.

## Slide 8: How to avoid Bouncing?
The digital functions in general and microcontrollers don’t like to see input signals wandering around in the undefined region between a “good” logic 0 and a “good” logic 1. ,
In 1934, a young graduate student named Otto Herbert Schmitt invented a circuit known as the Schmitt trigger (this invention was a result of Otto’s study into the propagation of neural impulses in the nerves of squids- a kind of sea fish). The best way to describe this is by means of a figure as illustrated in the next slide.

## Slide 9: How to avoid Bouncing?
Single threshold
Dual thresholds
Hysteresis

## Slide 10: How to avoid Bouncing?
A standard buffer has only a single switching threshold, which means that a noisy signal including a signal with a bit of ripple on it, can result in multiple transitions at the output.
In comparison, a Schmitt trigger buffer that is, a buffer with a Schmitt trigger input, has two thresholds. The output changes only when the input crosses the upper threshold or the lower threshold. This dual-threshold action is called hysteresis (the dependence of the state of a system on its history), which implies that the trigger possesses memory.

## Slide 11: How to avoid Bouncing?
In the RC network, we use a simple SPST switch debounce circuit, we would add a Schmitt trigger buffer between the RC network and the microcontroller as illustrated below.

## Slide 12: How to avoid Bouncing?
We have shown a non-inverting Schmitt trigger buffer to keep things simple (i.e., all the signals going up and down in a common direction).
It is common to use an inverting Schmitt trigger buffer because inverting functions are faster than their non-inverting counterparts.

## Slide 13: Why we need Debouncing?
Bouncing often causes problems in the application where pressing the switch once should theoretically cause only one transition.
If we connect the switch button to a pin with an external interrupt enabled, we will get several interrupts from pressing the button just once. This behavior is normally not wanted and can cause multiple false button presses.
Example: Imagine using a button in a TV remote controller for the selection of a channel. If the button is not being debounced, one press can cause the remote to skip one or more channels.

## Slide 14: Types of Debouncing
We can remedy this problem by debouncing the switch. There are many ways to do this. There are two general ways of getting rid of the bounces:
  Hardware debouncing: adding circuitry that actually gets rid of the unwanted transitions.
  Software debouncing: adding code/program that causes the application to ignore the bounces.
  Digital Switch Debouncing: achieved in the same way as the software approaches
  Switch Debouncer using VHDL: The VHDL entity description is used.

## Slide 15: Hardware Debouncing
There are various implementations of circuits that can be used for eliminating the effect of switch debouncing right at the hardware level.
One of the most popular solutions using hardware is to employ a resistor/capacitor network with a time constant (t) longer than the time it takes the bouncing contacts to stop, i.e., t > tbounce. Often it is also followed by a Schmitt trigger which helps get rid of the capacitor voltage values midway between HIGH and LOW logic.
If we wish to preserve program execution cycles, it is best to use the hardware debouncing approach.

## Slide 16: Hardware Debouncing
In hardware debouncing, we may use a flip-flop to "latch" the signal, using a capacitor to absorb the bouncing periods.
Example Circuit
In the next slide, there is a simple circuit for debouncing a switch for digital logic. When the switch is closed, the voltage is pulled down through the switch, and when the switch is open, the output voltage is pulled HIGH through the resistor. The resistor prevents a short circuit when the switch is closed. The capacitor absorbs the bounces when the switch changes states. Keep in mind that this circuit will cause a short delay in switching because the capacitor takes time to charge through the resistor. The delay can be minimized by varying the values of the capacitor and resistor, but if the resistor is too small, it may not be sufficient to absorb the bounces.

## Slide 17: Hardware Debouncing
There is one problem: the capacitor exhibits a curve when charging, and parts of this curve will fall in the region where a logic chip is undecided whether to treat it as a HIGH or LOW. To fix this, a Schmitt trigger is added to the output.
Without a Schmitt trigger:
With a Schmitt trigger:
Remember that the 7414 Schmitt trigger will invert the signal.

## Slide 18: Hardware Debouncing
Circuit Design using the 7414 is a Schmitt trigger (inverting type buffer) with the input hysteresis:
The equation for discharging a capacitor is given by-
Debouncing circuit design using the 7414 Schmitt trigger (inverting type buffer)

## Slide 19: Hardware Debouncing
The circuit’s operation can be explained by looking at the equivalent circuits formed in the two switching states, e.g., open and closed.
Now, CLOSE the switch:
The capacitor will discharge via R2.
In time, C1 will discharge and Vb will reach 0 V.
Therefore, the output of the inverting Schmitt trigger will be a logic 1.
Starting with the switch OPEN:
The capacitor C1 will charge via R1 and D1.
In time, C1 will charge and Vb will reach within 0. 7 V of Vcc.
Therefore, the output of the inverting Schmitt trigger will be a logic 0.

## Slide 20: Hardware Debouncing
What about the bounce conditions?
If bounce occurs and there are short periods of switch closure or opening, the capacitor will stop the voltage at Vb immediately reaching Vcc or GND. Although bouncing causes slight charging and discharging of the capacitor, the hysteresis of the Schmitt trigger input stops the output from switching.
What about the diode?
The resistor R2 is required as a discharge path for the capacitor. Without it, C1 will be shorted when the switch is closed. Without the diode, D1, both R1 and R2 would form the capacitor’s charging path when the switch is open. The combination of R1 and R2 increases the capacitor’s charging time, and thus slows down the circuit. However, when the switch is closed, R1 is connected across the supply rails to limit the current flow to the circuit.

## Slide 21: Hardware Debouncing
Numerical Example:
A CMOS device like the 74AHCT14 dribbles about an mA from the inputs.
Both R1 and R2 control the capacitor’s charging time, and so set the debounce period for the switch open state.
The equation for charging is:

## Slide 22: Hardware Debouncing
Numerical Example:
The goal is to select values that ensure the capacitor’s voltage stays above the Vth, the threshold at which the gate switches till the switch stops bouncing.
Most of the switches exhibit bounce times well under 10 ms, so the use of this value would be a conservative choice. Now increase that by the bounce duty cycle. Based on experimental data, we can expect about a 50% duty cycle, giving us 20 ms of a time period.
Rearranging the time constant formula to solve for R (the cost and size of capacitors vary widely so it is the best option to select a value for C and then compute R) yields:

## Slide 23: Hardware Debouncing
Numerical Example:
The AHCT version has a worst-case Vth for a signal going low of 1.7 V.
Let us try with a 0.1 μF capacitor, since this is small, cheap, and solve for the conditions in which the switch is closed. The capacitor discharges through R2. If the power supply is 5 V (i.e., Vinitial = 5 V) then . Since a resistor with this value is not available, so we use 180 kΩ.
But the analysis ignores the gate’s input leakage current. A CMOS device like the 74AHCT14 dribbles about a μA from the inputs. That 180 kΩ resistor will bias the input up to 0.18V (V), uncomfortably close to the gate’s best-case switching point of 0.5 V. Therefore, change the capacitor’s capacitance to 1 μF and use 18 kΩ for R2.

## Slide 24: Hardware Debouncing
Numerical Example:
R1 + R2 controls the capacitor’s charging time, and so sets the debounce period for the condition when the switch opens. The equation for charging is:
Solving for R:
Vfinal is the final charged value of the 5 V power supply. Vth is the worst-case transition point for a high-going signal, which for our 74AHCT14 is 0.9 V. So, . R2 = 18 kΩ. Hence, R1 = 82 kΩ.

## Slide 25: Hardware Debouncing
Numerical Example:
The diode is an optional part needed only when the math goes haywire. It is possible, with the wrong sort of gate where the hysteresis voltages assume other values, for the formulas to pop out a value for R1 + R2 which is less than that of R2. The part forms a shortcut that removes R2 from the charging circuit. All the charge flows through R1.
Equations will be the same except that we have to take the voltage drop across the diode into account. Change Vfinal to 4.3 V (5 minus the 0.7 V of diode’s forward voltage drop) and solve for R1 again.
Be wary of the components’ tolerances! Standard resistors are usually ±5-10% and the capacitors are ±20% (for electrolytic) and ±30% (for small ceramic capacitors) are error prone from their nominal rating.

## Slide 26: Software Debouncing
Debouncing in hardware may give rise to additional cost, and it is more difficult to determine a good debouncing for all the push button switches that will be used. So, it may be preferable to debounce the switch in software.
Debouncing a switch in software is very simple. The basic idea is to sample the switch signal at a regular interval and filter out any glitches. There are a couple of approaches to achieving this. These approaches assume a switch circuit like that shown in the explanation of switch bounce- a simple push switch with a pull-up resistor.
While numerous algorithms exist to perform the debouncing function, we are going to limit ourselves to implementing two during the lab. Both approaches use a timer.

## Slide 27: Software Debouncing
Approach 1
The first approach uses a counter to time how long the switch signal has been low. If the signal has been low continuously for a set amount of time, then it is considered pressed and stable.
    1 Setup a counter variable, initialized to zero.
    2 Setup a regular sampling event, perhaps using a timer. Use a period of about 1 ms.
    3 On a sample event:
    4 if the switch signal is HIGH then
    5 RESET the counter variable to ZERO
    6 SET internal switch state to released
    7 else
    8 Increment the counter variable to a maximum of 10
    9 end if
    10 if counter=10 then
    11 SET internal switch state to pressed
    12 end if

## Slide 28: Software Debouncing
Approach 2
The second approach is similar to the first but uses a shift register instead of a counter. The algorithm assumes an unsigned 8-bit register value, such as that found in 8-bit microcontrollers.
    1 Setup a variable to act as a shift register and initialize it to xFF.
    2 Setup a regular sampling event, perhaps using a timer. Use a period of about 1 ms.
    3 On a sample event:
    4 SHIFT the variable towards the most significant bit
    5 SET the least significant bit to the current switch value
    6 if shift register value = 0 then
    7 SET internal switch state to pressed
    8 else
    9 SET internal switch state to released
    10 end if

## Slide 29: Software Debouncing
There are two more approaches of software debouncing.
In the first technique, we wait for a switch closure, then test the switch again after a short delay (15 milliseconds or so). If it is still closed, we determine that the switch has changed state.
In the second technique, we test the switch periodically to see if it has changed its state.

## Slide 30: Software Debouncing
When working with microcontrollers, we can deal with switch bounce in a different way that will save both hardware space and money. Some programmers do not care much about bouncing switches and just add a 50 ms delay after the first bounce. This will force the microcontroller to wait 50 ms for the bouncing to stop, and then continue with the program. This is actually not a good practice, as it keeps the microcontroller occupied with waiting out the delay.
Another way is to use an interrupt for handling the switch bounce. Be aware that the interrupt might be fired on both the rising and falling edge, and some microcontrollers might stack up one waiting interrupt.

## Slide 31: Software Debouncing
The following is a simple software debounce code for Arduino written in IDE
int inPin = 7; // the number of the input pin
int outPin = 13; // the number of the output pin
int counter = 0; // how many times we have seen new value
int reading; // the current value read from the input pin
int current_state = LOW; // the debounced input value
// the following variable is a long because the time, measured in milliseconds,
// will quickly become a bigger number than can be stored in an int.
long time = 0; // the last time the output pin was sampled
int debounce_count = 10; // number of millisecond/samples to consider before declaring a debounced input
void setup()
{
pinMode(inPin, INPUT);
pinMode(outPin, OUTPUT);
digitalWrite(outPin, current_state); // setup the Output LED for initial state
}

## Slide 32
void loop()
{
// If we have gone on to the next millisecond
if(millis() != time)
{
reading = digitalRead(inPin);
if(reading == current_state && counter > 0)
{
counter--;
}
if(reading != current_state)
{
counter++;
}
// If the Input has shown the same value for long enough let's switch it
if(counter >= debounce_count)
{
counter = 0;
current_state = reading;
digitalWrite(outPin, current_state);
}
time = millis();
}
}

## Slide 33: Software Debouncing
The following program toggles two LEDs connected to a PIC microcontroller.
// INCLUDES
#include <stdio.h>
#include <stdlib.h>
#include <xc.h>
// CONFIG
#pragma config FOSC = INTOSCIO // Oscillator Selection bits (INTOSC oscillator: I/O function on RA6/OSC2/CLKOUT pin, I/O function on RA7/OSC1/CLKIN)
#pragma config WDTE = OFF // Watchdog Timer Enable bit (WDT disabled)
#pragma config PWRTE = OFF // Power-up Timer Enable bit (PWRT disabled)
#pragma config MCLRE = ON // RA5/MCLR/VPP Pin Function Select bit (RA5/MCLR/VPP pin function is MCLR)
#pragma config BOREN = ON // Brown-out Detect Enable bit (BOD enabled)
#pragma config LVP = ON // Low-Voltage Programming Enable bit (RB4/PGM pin has PGM function, low-voltage programming enabled)
#pragma config CPD = OFF // Data EE Memory Code Protection bit (Data memory code protection off)
#pragma config CP = OFF // Flash Program Memory Code Protection bit (Code protection off)
// DEFINITIONS
#define _XTAL_FREQ 4000000
#define LED1 PORTBbits.RB3
#define LED2 PORTBbits.RB2
#define BTN PORTBbits.RB5

## Slide 34
// VARIABLES
char BTN_pressed = 0;
char BTN_press = 0;
char BTN_release = 0;
char BounceValue = 500;
// MAIN PROGRAM
int main(int argc, char** argv) {
// Comparators off
CMCON = 0x07;
// Port directions, RB5 input, the rest is output
TRISA = 0b00000000;
TRISB = 0b00100000;
// Port state, all low
PORTA = 0b00000000;
PORTB = 0b00000000;
// Starting with LED1 high and LED2 low
LED1 = 1;
LED2 = 0;

## Slide 35
while (1)
{
// If BTN is pressed
if (BTN == 1)
{
// Bouncing has started so increment BTN_press with 1, for each "high" bounce
BTN_press++;
// "reset" BTN_release
BTN_release = 0;
// If it bounces so much that BTN_press is greater than Bounce value then the button must be pressed
if (BTN_press > Bouncevalue)
{
// This is initial value of BTN_pressed.
// If program gets here, button must be pressed
if (BTN_pressed == 0)
{
// Toggle the LEDs
LED1 ^= 1;
LED2 ^= 1;
// Setting BTN_pressed to 1, ensuring that we will not enter this code block again
BTN_pressed = 1;
}

## Slide 36
BTN_press = 0;
}
}
else
{
// Increment the "low" in the bouncing
BTN_release++;
BTN_press = 0;
// If BTN_release is greater than Bouncevalue, we do not have a pressed button
if (BTN_release > Bouncevalue)
{
BTN_pressed = 0;
BTN_release = 0;
}
}
}
return (EXIT_SUCCESS);
}

## Slide 37: Interrupts
An interrupt is the automatic transfer of software execution in response to a hardware event that is asynchronous with the current software execution.
The hardware event can either be a busy to ready transition in an external I/O device (like the UART input/output) or an internal event (like bus fault, memory fault, or a periodic timer).

## Slide 38: Why do we need it?
Let’s think about a real-life example:
You are heating up your food using the microwave.
In this case, you can either:
  Stare at the microwave while it heats up the food
  Go about your life normally and go to the microwave when you get the signal that the food has been heated up

## Slide 39: Why do we need it? (Cont.)
Which of the above-mentioned options do you think is more efficient?
Usually, we want to go about our life while the food is being heated up.
This is because we want to make efficient use of our time.
It is very similar for processors as well.
We hear the ting sound from the microwave, stop what we are doing, and go to take out the heated food.
This ‘ting’ sound is an interrupt.

## Slide 40: Why do we need it? (Cont.)
Similarly, if the processor is waiting for some conditions to be fulfilled to perform a specific task (task 1):
  It can wait and halt other processes till the conditions for that task is fulfilled.
  It can execute the normal instructions and halt them for a brief time once the conditions for task 1 have been fulfilled, finish task 1 and go back to executing the main routine.

## Slide 41: Why do we need it? (Cont.)
Clearly, the 2nd option is better for maximizing the processor’s resource utilization.
This is where interrupts come in handy.
When the conditions for task 1 has been met, it can simply trigger an interrupt, stop the main routine to complete the task and once finished go back to the main routine.

## Slide 42: Interrupt Conditions
Device arm
NVIC enable
Global enable
Interrupt priority level must be higher than current level executing
Hardware event trigger

## Slide 43: Arming the device
To arm a device means to allow the hardware trigger to interrupt.
To disarm a device means to shut off or disconnect the hardware trigger from the interrupts.

## Slide 44: Nested Vector Interrupt Controller (NVIC)
The module that controls all the interrupts
NVIC is device specific

## Slide 45: Global Enable
The main interrupt flag
This is used to turn all the interrupts on or off
Example: sei(); //globally enable interrupt

## Slide 46: Priority
Interrupts have priorities.
Suppose, 2 different tasks must be done at the same time.
The tasks must be assigned relative priorities to decide which will be performed first

## Slide 47: Trigger
An asynchronous event which causes the interrupt
For example, the push button press during experiment 4 in our MES Lab can be a trigger.
It can cause an interrupt which is registered by the module and is reacted to.
However, what if all the conditions are not met but a trigger flag is set?
In this case, rather than the request being dismissed, it is held pending, postponed until a later time.

## Slide 48: What happens after a trigger?
Once the interrupt is triggered and processed, the interrupt flag is cleared.
Clearing the interrupt flag is called acknowledgement.

## Slide 49: Interrupt Service Routine (ISR)
The module that is executed when a hardware requests an interrupt.
There may be 1 large ISR handling all the interrupt requests, or many small ISRs handling the many interrupts (interrupt vectors).
Example :
ISR (TIMER0_OVF_vect) //enabling overflow vector inside Timer0 using an ISR
ISR (TIMER0_COMPA_vect) //This is the Timer0 Compare ‘A’ interrupt service routine.
Remember, the ISR is a separate routine and requires a separate flowchart to represent.

## Slide 50: General Rules for ISR
The ISR should execute as fast as possible.
  The interrupt should occur when it’s time to perform the required action
  The ISR should perform the action
  The ISR should end and return to the main function right away.
Placing backward branches (busy, wait, iterations) inside the ISR should be avoided.
The percentage of time spent executing ISR should be small when compared to the time between interrupt triggers.

## Slide 51: References
ATMega328 manual
http://www.ganssle.com/debouncing-pt2.htm
https://mansfield-devine.com/speculatrix/2018/04/debouncing-fun-with-schmitt-triggers-and-capacitors/
http://users.ece.utexas.edu/~valvano/Volume1/E-Book/C12_Interrupts.htm

## Slide 52: Thanks for attending….
?